## Slide 1: Hardware Software Platforms Project Presentation
Smart Traffic Lights 2
FLAMENT Dorian - NGUYEN Thuy hai
Dorian.Flament@student.umons.ac.be
Thuy-hai.Nguyen@student.umons.ac.be
Notes: Marine

## Slide 2: Introduction
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
What is the point of smart traffic lights ?
Pollution reduction
Time gain
Priority for emergency vehicles
Notes: Marine
Dire que parfois il n’y a personne sur l’autre route, mais il faut attendre quand même. Pour les gros véhicules ça prend du temps et ça pollue de les faire démarrer, et en plus si c’est une ambulance ils doivent passer en priorité. S’il y a 10 voitures sur une voie et 1 sur l’autre, c’est mieux d’en arrêter qu’une pour l’environnement.

## Slide 3: Tutorial version
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Objectives
Detect cars on roads
Traffic lights control based on number of cars in each road
Notes: Dorian

## Slide 4: Components
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Traffic Lights with LEDs
Raspberry PI
Manage cars detection
Manage cars counter
Send signals to leds
Notes: Dorian

## Slide 5: Components
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Webcam
In original tutorial, PiCamera
was used.
cam = PiCamera()
cam.resolution=(480,480)
cam.framerate=30
raw=PiRGBArray(cam, size=(480,480))
-> Code adapted to work with
any USB camera.
cam=cv2.VideoCapture(0)
cam.set(4,480) #Width=480
cam.set(5,480) #Height=480
cam.set(6,30) #FrameRate = 30
Notes: Dorian
Nous avons nous-mêmes modifié le code de base pour que ça marche avec une simple webcam usb

## Slide 6: Components
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
USB
Pin 21
Pin 23
Pin 25
Pin 16
Traffic light for vertical road
Traffic light for
horizontal road
82 Ω
82 Ω
82 Ω
82 Ω
Notes: Dorian

## Slide 7: Global view
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Webcam
Traffic Lights
Notes: Dorian
On a construit nous-mêmes une structure pour pouvoir installer la webcam et tester le code.
On voit que les traffic lights et la webcam sont reliées à la Rpi, et à droite on place des voitures pour pouvoir tester.

## Slide 8: Block diagram
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Video stream from webcam
InitVert = 0
InitHor = 0
Is webcam working ?
Close all windows
Release webcam
Capture frame
Treatment
Find contours
Ncars
Counter and analysis
Show different streams
Stop key
No
No
Yes
Yes
Notes: Marine

## Slide 9: Block diagram
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Car in vertical lane ?
Vert
Vert + 1
Car in horizontal lane ?
Hor + 1
Hor
Hor = InitHor ?
Vert = InitVert ?
Traffic lights don’t change
Vert < Hor ?
Counter and analysis
Green light for hor
Red light for vert
Green light for vert
Red light for hor
Car = Ncars ?
No
No
No
No
No
Yes
Yes
Yes
Yes
Yes
Notes: Marine
Détails du bloc counter and analysis

## Slide 10: Block diagram
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Video stream from webcam
InitVert = 0
InitHor = 0
Is webcam working ?
Close all windows
Release webcam
Capture frame
Treatment
Find contours
Ncars
Counter and analysis
Show different streams
Stop key
No
No
Yes
Yes
Notes: Marine

## Slide 11: Frame treatment
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Capture frame
Treatment
Library used: openCV (cv2)
Transform frame into array
Convert RGB to HSV
Threshold the HSV to exclude black and white
(road and strips)
4. Blur to ignore details
5. Dilate 10 times
6. Erode
7. Dilate 5 times
8. Threshold
Notes: Dorian

## Slide 12: Find contours
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Enclose vehicles with circle
Find radius and center
Coordinates of center are used to determine position on the road
Notes: Dorian

## Slide 13: Modifications
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Original code was not working fine.
Some modifications made by us to improve the code :
Increase dilatation for detection to be adapted to all kind of cars
View of all different masks (blur, dilate, erode) to see different steps of detection
Put all masks in one window for more visibility
Correct limits of the road to be adjusted to our structure
Make code work for any USB webcam
Notes: Dorian

## Slide 14: Next step ?
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Code could still be improved …
Notes: Marine

## Slide 15: Improved Version
Objectives
  Give the priority to large vehicles like fire engines in order to manage emergency, decrease pollution and traffic jams
  Automatic detection of road limits in order to adapt the system to all sizes of road of cross crossroads
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Notes: Marine

## Slide 16: Improved Version
Block Diagram
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Calibration of the roads
Limits of road detected
Detection of priority vehicle on a road
Yes
No
Green light for this road
Tutorial version algorithm is used
Coordinates of the calibration objects detected
Notes: Marine

## Slide 17: Improved Version 1
Improvement 1 : Automatic Calibration
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Calibration objects to detect the coordinates of the crossroads limits
Notes: Marine

## Slide 18: Improved Version 1
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
4 crossroads limits
Frame divided into 4 parts: each calibration object is
associated with a zone
Accurate calibration
Notes: Marine
Détailler la calibration avec la position des plots dans chaque quartier (couper l’image en 4)
Associer un carré jaune à un des coins du carrefour
On obtient 4 coins.
Détection précise car coordonnées correspondantes sont quasi égales

## Slide 19: Improved Version 1
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Correct calibration: vehicles in crossroads and outside
road limits are not taken into account
Notes: Marine

## Slide 20: Improved Version 2
Improvement 2 : Priority vehicles
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Rectangle are used to frame : more accurate to detect the size of a vehicle -> area of rectangle is calculated to determine size
Originally
Improved
Notes: Dorian

## Slide 21: Improved Version 2
Improvement 2 : Priority vehicles
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
When a large vehicle appears on a road
(area > threshold) :
The other vehicles are not counted
Green light for this road
Notes: Dorian

## Slide 22: Prospect of improvement
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
What could be even more improved:
Adaptation to more complex crossroads
Priority for emergency vehicles over priority for trucks (specific colors)
Notes: Dorian

## Slide 23: Project presentation video
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Youtube links:
Base tutorial:
https://www.youtube.com/watch?v=jQJlSoAfE3g&t=25s
Improved version 1:
https://www.youtube.com/watch?v=-3C68o-8WWs&t=21s
Improved version 2:
https://www.youtube.com/watch?v=j2LM9ZPuFI4
Notes: Dorian

## Slide 24: Useful links
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Youtube channel:
https://www.youtube.com/channel/UCRLHQksECPiZ9VwZONcNINQ
Base tutorial:
http://www.instructables.com/id/Smart-Traffic-Light/
GitHub
https://github.com/Twitwi96/Smart-traffic-light-2
Notes: Dorian
Remercier pour l’attention
Dire qu’on va montrer une vidéo

## Slide 25: Thank you for your attention !
Smart Traffic Lights 2 – FLAMENT Dorian & NGUYEN Thuy hai
Notes: Dorian
Remercier pour l’attention
Dire qu’on va montrer une vidéo